## Slide 1
0
10
20
30
40
50
mbgl
JALDRISHTI 01 / 16
JALDRISHTI
GROUND SURFACE · 0.00 MBGL
A GROUNDWATER MONITORING
AND PREDICTIVE ALERT SYSTEM
MINOR PROJECT B.TECH · COMPUTER SCIENCE & ENGINEERING INVERTIS UNIVERSITY 2026

## Slide 2
0
10
20
30
40
50
mbgl
JALDRISHTI 02 / 16
THE PROBLEM / SCALE
INDIA RUNS ON WATER
IT CANNOT SEE
63%
OF IRRIGATED AREA
Fed from groundwater, not surface canals or rivers.
85%
OF RURAL DRINKING WATER
Drawn from wells and borewells across the country.
1st
LARGEST USER, WORLDWIDE
India extracts more groundwater than any other nation.
The resource is invisible, so it is managed reactively. A district usually learns its water table has fallen only after wells begin to fail.

## Slide 3
0
10
20
30
40
50
mbgl
JALDRISHTI 03 / 16
THE PROBLEM / THE DATA
THE MEASUREMENTS EXIST.
THEY JUST CAN'T BE READ.
The Central Ground Water Board monitors a national network of observation wells and publishes every reading, every year — as hundreds of pages of tabulated PDF.
A PDF table cannot be queried, ranked, or joined to anything else.
Nothing in the document compares one region against another.
Nothing in it looks forward — there is no station-level forecast.
The raw depth figure isn't comparable: 10 m is routine in one aquifer and alarming in the next.

## Slide 4
0
10
20
30
40
50
mbgl
JALDRISHTI 04 / 16
THE SYSTEM / FIVE LAYERS
FROM PUBLISHED PDF
TO A DECISION SURFACE
LAYER 01
EXTRACTION
Batch table extraction from the source report, with generated station identifiers.
→ raw records
LAYER 02
PREPARATION
Cleaning, quality control, and a per-station historical baseline.
→ clean set + baselines
LAYER 03
ANALYTICS
The GAVI score, then a prioritised alert engine over score and trend.
→ scored + alerted
LAYER 04
FORECASTING
One- and three-year projections per station, converted back into scores.
→ forward alerts
LAYER 05
PRESENTATION
An interactive dashboard built for officials, not analysts.
→ live dashboard
Each layer persists its own dataset, so any stage can be re-run and refined without repeating the expensive ones upstream.

## Slide 5
0
10
20
30
40
50
mbgl
JALDRISHTI 05 / 16
THE SYSTEM / WHAT WE ASSEMBLED
A DECADE OF READINGS,
MADE QUERYABLE
86,912
OBSERVATIONS
9,545
MONITORING STATIONS
713
DISTRICTS
31
STATES & UTS
Covering 2015 to 2024. January readings are used throughout, so every station is compared against itself at the same point in the annual recharge cycle — the seasonal swing is removed by construction, not by modelling.

## Slide 6
0
10
20
30
40
50
mbgl
JALDRISHTI 06 / 16
THE INDEX / CORE CONTRIBUTION
GAVI: ONE NUMBER
THAT TRAVELS
GAVI = 100 × [ 1 − ( WL_current − WL_min ) ÷ ( WL_max − WL_min ) ]
Each station is rescaled against its own historical extremes. 100 is that station at its best on record; 0 is its worst.
Because the normalisation is station-specific, local geology and aquifer type are absorbed into the baseline — which is what makes a score of 30 in Rajasthan mean the same thing as a score of 30 in Odisha.

## Slide 7
0
10
20
30
40
50
mbgl
JALDRISHTI 07 / 16
THE INDEX / SCORE TO ACTION
EVERY BAND NAMES
A DECISION
SAFE
75 – 100
Good availability. Continue routine monitoring.
WATCH
50 – 74
Moderate stress developing. Increase observation frequency.
STRESSED
25 – 49
Significant depletion. Regulate demand and plan recharge.
CRITICAL
0 – 24
Severe deficit. Emergency intervention and extraction control.
A district officer reads a category and an action — never a hydrological unit.

## Slide 8
0
10
20
30
40
50
mbgl
JALDRISHTI 08 / 16
ALERTS / RESOLVED BY PRIORITY
ONE STATION,
ONE ALERT, ONE YEAR
01
CRITICAL_GROUNDWATER
GAVI below 25
02
DEPLETION_WARNING
GAVI below 50 and the table is falling
03
SUDDEN_DROP
Level falls 2.0 m or more in one year
04
RECOVERY_SIGNAL
Level rises 1.0 m or more in one year
05
NORMAL
No rule satisfied; routine monitoring
The ladder is strictly ordered — severity always outranks trend, so no station can carry contradictory signals.

## Slide 9
0
10
20
30
40
50
mbgl
JALDRISHTI 09 / 16
ALERTS / TRUST
AN ALERT NOBODY
BELIEVES IS WORTHLESS
A single bad reading — a faulty gauge, one anomalous season — must not put a district into emergency response. Two filters stand between the data and the siren:
2×
PERSISTENCE CHECK
A critical alert must appear in two or more consecutive observations before it is treated as confirmed.
3obs
ROLLING WINDOW
A three-observation window smooths transient spikes so measurement noise cannot trigger a response.

## Slide 10
0
10
20
30
40
50
mbgl
JALDRISHTI 10 / 16
FORECAST / THE MODEL
DELIBERATELY SIMPLE,
ON PURPOSE
WL_future = WL_last + mean historical ΔWL
Each station is projected at one-year and three-year horizons, clipped to the physically meaningful range of 0–50 mbgl, then converted back into a GAVI score against the same baseline.
Two reasons the first model is a transparent trend and not a neural network: it can be explained to the official acting on it, and it sets the benchmark any machine-learning model has to beat to justify its opacity.

## Slide 11
0
10
20
30
40
50
mbgl
JALDRISHTI 11 / 16
FORECAST / BACKTESTED, NOT ASSERTED
FIT ON 2015–2022.
PREDICT 2023. SCORE IT.
WITHIN 1 M
61.7%
WITHIN 2 M
80.7%
1.38m
MEAN ABSOLUTE ERROR
19.2%
MAE AS A SHARE OF MEAN LEVEL
Four stations in five land within two metres. That is honest baseline accuracy — reported as measured, and the number the next model must improve on.

## Slide 12
0
10
20
30
40
50
mbgl
JALDRISHTI 12 / 16
FINDINGS / LATEST YEAR
WHAT THE DATA
ALREADY SAYS
43.3%
OF STATIONS UNDER STRESS (GAVI BELOW 50)
1,109
CRITICAL ALERTS ACTIVE
54.1
NATIONAL AVERAGE GAVI
Every one of these figures was already sitting in the published record. It was spread across hundreds of pages of tabulated PDF, where it is unreadable at a glance and unusable as a trigger for action.

## Slide 13
0
10
20
30
40
50
mbgl
JALDRISHTI 13 / 16
FINDINGS / THREE YEARS OUT
AND WHERE
IT IS HEADING
PROJECTED GAVI CATEGORY AT THE THREE-YEAR HORIZON — 3,636 STATIONS WITH SUFFICIENT RECORD
Safe 1,476 · 40.6%
Watch 396 · 10.9%
Stressed 408 · 11.2%
Critical 1,356 · 37.3%
1,356 stations are projected to be critical within three years, against 1,263 flagged at the one-year horizon. Those are named stations in named districts — a work list, not a statistic.

## Slide 14
0
10
20
30
40
50
mbgl
JALDRISHTI 14 / 16
DELIVERY / THE PRODUCT
SIX PAGES, ONE
BROWSER TAB
OVERVIEW
National position at a glance — headline counts and the current distribution.
GAVI ANALYSIS
Score distributions and category movement over the decade.
ALERTS
Live alert counts by type, filtered down to state and district.
GEOGRAPHIC
Clustered station maps and district ranking by stress ratio.
FORECASTING
One- and three-year projections with forward-looking alerts.
STATION EXPLORER
The full history of any single well, against its own baseline.
No installation, no query language, no hydrology degree required.

## Slide 15
0
10
20
30
40
50
mbgl
JALDRISHTI 15 / 16
DELIVERY / HOW IT'S BUILT
OPEN SOURCE,
END TO END
LANGUAGE
Python 3.11
EXTRACTION
Camelot · Ghostscript · pypdf · OpenCV
PROCESSING
pandas · NumPy · Jupyter
INTERFACE
Streamlit · Plotly · Folium
DEPLOYMENT
Docker · AWS EC2 · Git
Development cost is effectively nil: the toolchain is free, the data is published by the Government of India, and 86,912 records fit comfortably in memory on a commodity laptop. The only recurring cost is optional hosting.

## Slide 16
0
10
20
30
40
50
mbgl
JALDRISHTI 16 / 16
IN CLOSING /
SHORTEN THE DISTANCE BETWEEN MEASUREMENT AND INTERVENTION.
The readings were already being taken. JalDrishti turns them into a score that travels, an alert that can be trusted, and a forecast that arrives before the wells do.
JALDRISHTI SOURCE: CENTRAL GROUND WATER BOARD, 2015–2024